|  | National Institute of Plant Health Management Department of Agriculture & Cooperation Ministry of Agriculture Government of India |  |
| --- | --- | --- |
| Telephone: 9140-24015374 E-mail: niphm@nic .in Tele-Fax: 9140-24015346 | Rajendra Nagar, Hyderabad – 500 030 http://niphm.gov.in |

F. No. 8.1.1.2/PBS/Equip/NIPHM/13-14/13				       Dated : 10/07/2013

To

(As per list *)

# *(The tender document is also being uploaded on the NIPHM website http://niphm.gov.in and the other prospective bidders can make use of the document down loaded from the website)

Sub:- Limited Tender for Procurement of Laboratory Equipment for Plant Biosecurity Division – reg.

* * *

Sir/Madam,

National Institute of Plant Health Management (NIPHM) invites ‘Sealed Bids’ from the reputed manufacturers/authorized distributors/dealers for procurement of Laboratory Equipment for Plant Biosecurity Division Detailed terms and conditions and list of items required may be downloaded from the NIPHM website http://niphm.gov.in

The schedule of receipt and opening of quotations is as under:-

Last date and time for receipt of bids 	::	14:00 hrs on

25/07/2013.

Date & Time for opening of bids		::	15:00 hrs on

25/07/2013.

Administrative Officer

for Registrar

TERMS AND CONDITIONS:

- GENERAL INSTRUCTION TO BIDDING:

- Any offer made in responses to this tender when accepted by NIPHM will constitute a contract between the parties.

- Tenderer is exempted from  Earnest Money Deposit

- The Contract shall be interpreted under Indian laws and all disputes will be resolved within Hyderabad Jurisdictions. In case of any dispute, the decision of NIPHM, Hyderabad shall be final and binding.

- The supplier will be fully responsible for any loss in transit and will also be responsible for safe delivery of the goods/stores in good conditions at NIPHM.

- The quantity of items may increase or decrease at the time of award of purchase order.

- Quotation should be valid for a minimum period of SIXTY DAYS from opening of tender.  The sealed quotation duly superscribing on the envelop “Quotation for supply of Laboratory Equipment for Plant Biosecurity Division with tender no. and due date” should reach on or before the specified date and time to the Registrar NIPHM, Rajendranagar, Hyderabad-500 030.

- The NIPHM takes no responsibility for delay, loss or non-receipt of quotations/documents sent by post and reserves the right to accept or reject any part/full of the quotation without assigning any reasons whatsoever.

- Tenders received after due date and time shall be rejected.

- The rates quoted should be inclusive of all charges such as Octroi, packing, forwarding, insurance and loading, unloading, freight and clearance etc. and bidder should undertake to supply goods at NIPHM at his cost.

- The VAT/Sales/General taxes where legally leviable and intended to be claimed should be distinctly shown along with the price quoted.  Where this is not done it will be treated that the price is inclusive of VAT & other taxes. VAT/CST registration No. and date of its validity should be indicated. This Institute will not provide “C” & “D” forms, hence quote for the taxes actually leviable. The firm must quote their TIN No. , PAN No., (IT returns) VAT registration no. etc. in the quotation (attested copies to be enclosed).

- The rates should be mentioned clearly in both figures and words for each item in the quotation.  If there is any variation in figures and words rates quoted in words will be taken in to consideration. The overwriting, cutting, erasing, if any should clearly be indicated duly attested.

- Corrupt or Fraudulent Practices: Bidders should observe the highest standard of ethics during the procurement and execution of such contracts.  “Corrupt practice” means the offering, giving, receiving or soliciting of anything of value to influence the action of public official in the procurement process or in contract execution, and “Fraudulent practice” means a misrepresentation of facts in order to influence a procurement process or the execution of a contract to the detriment of the Purchaser and includes collusive practice among Bidders (prior to or after bid submission) designed to establish bid prices at artificial non-competitive levels and to deprive the Purchaser of the benefits of free and open competition.

NIPHM will reject a proposal for award if it is found that the Bidder recommended for award has engaged in corrupt or fraudulent practices in competing for the contract in question.

- CONDITIONS OF CONTRACT

- Sealed Quotations will be accepted from authorized dealers/ distributors/manufacturers for supply of Laboratory Equipment in accordance with our specifications.

- In case of dealer/distributor should enclose the authorization letter from the manufacturer.  Experience of manufacturer will be taken into account in respect of authorized dealer and distributor.

- In respect of manufacturers Gross Annual Turnover of Rs. 25.00 lakhs. In respect of authorized dealer, the turnover of the manufacturer will be taken into account. In respect of other bidder’s the annual gross turn over should be at least Rs. 20.00 lakhs during last  financial year, for which they have to enclose copy of the annual accounts duly signed and attested by a Chartered Accountant. Proof to be submitted.

Turnover not applicable to Registered Suppliers with NIPHM/DGS&D/CRIDA

- The manufacturer should have at least 3 years of experience in dealing/supplying of laboratory equipments, for which they have to enclose copies of purchase orders.  Experience of the manufacturer will be taken into account in respect of authorized dealer/distributor

- The NIPHM does not undertake any responsibility for issue of import licence where it may be required for the supply of the stores and acceptance of tender shall not imply such an undertaking on the part of NIPHM.

- TECHNICAL SPECIFICATIONS:

| S.No | Name of the item | Specifications | QTY |
| --- | --- | --- | --- |
| 1. | Microspin (small centrifuge) | 12 x 1.5/2 ml microtubes Adapter for 12 x 0.5ml microtubes Adapter for 12 x 0.2ml microtubes RPM: 100-14500k Operation time 1-30 min Input current=2.5A/60W Voltage=120 | 1 No. |
| 2. | Vortex | It should accommodate micro test tubes, PCR plates, deep well plates and Microtiter plate Power supply:230v, 50-60HZ Dimension: WXDXH)17X23X13cm Mixing frequency 300-3000rpm | 1 No. |

| S.No | Name of the item | Specifications | QTY |
| --- | --- | --- | --- |
| 3. | Wrist action shaker with timer | Type: hand motion shaker Speed : around 400 rpm Flask capacity: 8 of 250 ml flasks Shaking angle 0 to 18 degree Dimension: 25’WX13’HX16D” Maxi. Temperature 40 oc | 1 No. |
| 4. | Digital pH Meter - Bench top | pH range 1 to 14. Solution Temperature - 0-100oc | 1 No. |
| 5. | Hot plate with magnetic stirrer | Heating power 180 w Heating plate temperature 250 oc Stirring speed up to 1400 rpm Stirring capacity 500 ml Heating plate dimension: 118X118mm(4.6’’X4.6’’) Base dimension: (LXWXH)(200 mmX120mmX90mm) Control with LED indicator | 1 No. |
| 6. | Hot water bath | Capacity 20 litres. should hold different size of flasks Digital control systems. Temperatures range- room temperature to 99.9°C option for drainage plug | 1 No. |
| 7. | UV transilluminator | Fitten with short (254nm) Long (365nm) wave , Wave length UV tubes & Floureoscent tubes for day light Model No: SSI-63, Make: Shital LONG –WAVE 365 nm : L X W X H SHORT WAVE 254 nm: : 12” X 12” X 12” Visible Daylight Withseparate : 30 x 30 x 30 | 1 No. |
| 8. | Colony counter | Hand held portable Microcontroller based 6 digit LCD counter It should have Buzzer, Marker pen (aluminium) and counters with adopter and pen set | 1 No. |
| 9. | Horizontal gel electrophoresis (Medium size) | Should be suited for multiple-sample, rapid-screening applications. Should has a wide platform that can separate 30 samples per comb. | 1 No. |
| 10. | Mechanical Shaker with timer (rotary shaker) | Rotary Shaker with brushless induction motor, frequency drive to control speed from 20 to 300 rpm along with universal platform size: 24” X 24” Capacity: 16 Liters Clamps for holding conical flask 1000 ml - 9 500 ml - 12 250 ml - 15 | 1 No. |

| S.No | Name of the item | Specifications | QTY |
| --- | --- | --- | --- |
| 11. | Bacteriological Incubator shaker | Upto 170 litres Temperature: 5-700 C, Speed – maximum – 300 rpm Digital indicator with timer Universal platform tray with clamps for different sizes, Glass window, fitted with fluorescent tubes Tray for incubating Petri Plates | 1 No. |
| 12. | Compound Microscope with Photograph & image grabber facility | Trinocular 300 inclined 3600 rotating Eyepiece 10X Achromat objectives 4x, 10x, 40x and 100 x –oil immersion lens Quartz halogen 6V/30W with intensity control Digital Camera Live Resolution: 5 – 11 Mega pixels Focusable Lens: 12 mm with desired software with computer – 2 GB RAM, 500 GB HD, 4 USB Port, 17 TFT monitor, I-5, windows 7 | 1 No. |

- The Tenderer should submit along with their quotation, details of similar supply made to Training/Scientific/Technical Institutions of Govt./PSU/SAU/Pvt. Firms in India and the reference to that effect may be clearly mentioned and copies enclosed.  Catalogue /literature of the equipment/furniture quoted should be provided along with the quotation.

- The bidder should be quote AMC Charges for three years.

- Warranty should be provided at least for two years. The firm should provide details of after sales service.  The firm has to submit its willingness to this effect.

- Contract / Agreement

- The Successful firm(s) shall require to deposit 5% of the order value as Security deposit/Performance Security either by means of demand draft or irrevocable Bank Guarantee obtained from any nationalized/commercial banks in favour of National Institute of Plant Health Management (NIPHM), the Hyderabad which should be valid beyond 60 days beyond the date of completion of all contractual obligations of the supplier including warranty obligation. The security deposit will be released/discharged after 60 days of complication all contractual obligations of the supplier including warranty obligation

- The Performance Security shall be forfeited if the contractor declared successful fails to supply the stores as per specification mentioned in the purchase order or does not accept the assigned work for any reason, whatsoever.

- If the firm fails to deliver the goods within the stipulated delivery period as mentioned in the purchase order penalty of 2% per day of value of order shall be imposed/levied as liquidated damages

- Payment will be made within 15 days after receipt of material, installation and its final acceptance.

- PRICE SCHEDULE

- Name of the item:  Laboratory Equipment

| Sl. No. | Item Description | Make/ model | Unit | Quantity | Price (Rs.) | Sales Tax/VAT | TOTAL Amount (Rs.) |
| --- | --- | --- | --- | --- | --- | --- | --- |

- Annual Maintenance charges (for a minimum period of Three years) Rs. ________________

NOTE: 	1) 	Items should be delivered and installed at NIPHM

2)	Sales tax/VAT should be indicated clearly.

3)	Prices should be quoted only in Indian Rupees.

We are herewith undertaking that the details provided above are true and to abide by the terms and conditions contained in the bid document of NIPHM.

Signature of authorized official

(with seal and stamp)

Name		:

Designation	: