|  | National Institute of Plant Health Management Department of Agriculture & Cooperation Ministry of Agriculture Government of India |  |
| --- | --- | --- |
| Telephone : 9140-24011633/ e-mail : niphm@.nic .in Tele-Fax : 9140-24015346 |  | Rajendra Nagar, Hyderabad – 500 030 http://.niphm.gov.in |

F.No. 8.1/Equip/PBD/2013-14/				         		        	Date: 20.09.2013

CORRIGENDUM

The following amendments are issued to the tender no. 8.1/Equip/PBD/2013-14, dated 23-08-2013, in respect of procurement of ‘Microscopes’:

- Amendment:

| Existing Page no of tender document/ clause No | Existing condition | Amendment |
| --- | --- | --- |
| Page No 18-Technical specifications (Annexure II): For Research Purpose A2: Trinocular Stereo Zoom Microscope with Camera | Objectives : Antifungal objectives 0.08 – 4X zoom optics | Objectives : Antifungal objectives |

- Additional Equipment included for procurement of “Trinocular Phase Contrast Microscope with CCD Camera and IPP Software” (1 No.) as below

| Additional item |
| --- |
| Name of the Item | Amendment in Page No/Clause | Quantity |
| “Trinocular Phase Contrast Microscope with CCD Camera and IPP Software” | Clause 8.4 in Page no. 11, Technical Specification in Page no. 20(a) and Financial Bid (Annexure-III) in Page no. 21 | 1 No. |

.

- The last date for submission of the tender is extended upto  :  25.10.2013

- The Tenderers shall furnish as part of the bid, documents establishing the Tenderers eligibility to bid and its qualifications to perform the Contract if their tender is accepted.

The documentary evidence of the Tenderer's qualifications shall   be established to the satisfaction of NIPHM. However, the decision of Director General, NIPHM will be final in this regard.

  - Signing of Bids

Individual signing the tender or other documents connected with contract must

specify whether he signs as:

i) A “Sole proprietor” of the concern or constituted attorney of such sole proprietor;

ii)A partner of the firm, if it is a partnership firm in which case he must have authority to execute on behalf of the firm.

iii)Director or a Principal Officer duly authorized by the Board of Directors of the

Company, if it is a Company.

- The bids shall be typed or written in indelible ink and shall be signed by the Tenderer or a person or persons duly authorised to bind the Tenderer to the Contract. Tenderers are requested to sign each and every page of the tender document including Annexure(s) attached thereto.

- Any alterations, erasures shall be treated valid only if they are authenticated by full signature by the person or persons authorised to sign the bid. Tender documents should be free from over writing.

  - Details to be furnished in the Envelope-B i.e., Financial Bid

Firm Prices must be quoted only in the Financial Bid Form (Please see the “PART-B- FINANCIAL BID – ANNEXURE III)”.

The prices quoted should be both in figures and words. If there are any variations between the figures and words, price quoted in words only will be considered.

The items for research purpose for which customs exemption certificate will be provided

| S. No. | Name of the item | Qty. |
| --- | --- | --- |
| 1 | Trinocular Research Compound Microscope with Camera | 1 No. |
| 2 | Trinocular Stereo Zoom Microscope with Camera | 1 No. |
| 3 | Trinocular compound phase contrast microscope with fluorscene application along with high resolution cooled CCD camera | 1 No. |

The items for capacity building for which the customs duty exemption certificate will not be provided.

| S. No. | Name of the item | Qty. |
| --- | --- | --- |
| 1 | Binocular Research compound Microscope without camera | 9 Nos. |
| 2 | Stereo Zoom Binocular Microscope | 9 Nos. |
| 3 | Trinocular Phase Contrast microscope with CCD Camera and IPP software | 1 No. |

(please sign on each page)

11

Additional Item								Annexure - II

| S. No. | Description | Qty. |
| --- | --- | --- |
| B3 | TRINOCULAR PHASE CONTRAST MICROSCOPE WITH CCD CAMERA AND IPP SOFTWARE Microscope frame for 100W transmitted Halogen illumination set up and reflected microscopy with built-in filter holders for four filters (LBD, ND6, ND25 and GF), including hexagonal driver and immersion oil 8cc regulations, Wide field eyepiece 10X, FN22, Focusable, Lamp house for 100W halogen, Halogen bulb (12V100Watts), Power cord, Interference green contrast filter 45mm dia, Light balancing Day light filter, 45mm dia, Sextuple revolving nosepiece with a slot for analyzer or DICslider, Dust cover, oil. Stage: Ceramic surface mechanical stage with right-hand low drive control (long type), with individual torque adjustment for X - Y. Specimen holder for stage, left hand, for two specimens, thick type. Condenser: universal condenser for Phase,Bright field as well as Dark field studies. Objectives: 4X, 10X, 40X & 100X oil. Camera: HIGH RESOLUTION HIGH SPEED REAL TIME VIEWING 3.3 MP CCD CAMERA High quality 1/2” 3.3 mega pixel color CCD camera, Pixel pitch: 3.45 x 3.45 μm (Sony ICX282), Resolution up to 2048x1536 Pixel, Binning modes 2x2, 3x3, 4x4 in full color, 1.6µs to 17.9min in 1µs increments exposure/ integration control, Peltier thermoelectric cooling to 10 degress below ambient, 10 bits digital output, 30 fps full field of view. Software: Image-Pro Premier - USB license. | 1 No |

(Please sign on each page)

20(a)

Annexure III

PART – II

FINANCIAL BID

    - The list of items for research purpose for which the customs exemption certificate will be provided.

| S. No. | Item Description | Qty. | Catalogue/ Model No. | Price Rs. | Sales Tax/VAT | TOTAL Amount (Rs.) |
| --- | --- | --- | --- | --- | --- | --- |
| 1 | Trinocular Research Compound Microscope with Camera | 1 No. |  |  |  |  |
| 2 | Trinocular Stereo Zoom Microscope with Camera | 1 No. |  |  |  |  |
| 3 | Trinocular compound phase contrast microscope with fluorscene application along with high resolution cooled CCD camera | 1 No. |  |  |  |  |

    - The list of items for capacity building for which the customs exemption certificate will not be provided.

| S. No. | Item Description | Qty. | Catalogue/ Model No. | Price Rs. | Sales Tax/VAT | TOTAL Amount (Rs.) |
| --- | --- | --- | --- | --- | --- | --- |
| 1 | Binocular Research compound Microscope without camera | 9 Nos. |  |  |  |  |
| 2 | Stereo Zoom Binocular Microscope | 9 Nos. |  |  |  |  |
| 3 | Trinocular Phase Contrast microscope with CCD Camera and IPP software | 1 No. |  |  |  |  |

We are herewith undertaking that the details provided above are true and to abide by the terms and conditions contained in the bid document of NIPHM.

Signature of authorised official

(With seal and stamp)

Name :

Designation:

Note :	1) Annual Maintenance charges (for a minimum period of Three years) beyond 3 years warranty

should be quoted separately for each item

2) Items should be delivered and installed at NIPHM.

3) Sales tax/VAT should be indicated clearly.

4) Customs duty Exemption Certificate will be provided in respect of research items.

(please sign on each page)

21